## Slide 1
SafeSeaNet Architecture
Saint Petersburg
23-24 July 2008
Lazaros Aichmalotidis
Unit C.2 – Vessel Traffic and Ship Reporting

## Slide 2: Traffic Monitoring Directive 2002/59
Large political pressure
One critical question
“How is it possible that we do not
know what is sailing in front of
our coastline”
Directive 2002/59/EC aims at establishing in the Community a vessel traffic monitoring and information system.
SafeSeaNet (SSN) aims at developing a European Platform for Maritime Data Exchange between maritime administrations of the Member States (network for ship and cargo movements)
Allow MS to react more efficiently in crisis situation

## Slide 3: SSN needs information
  Data providers
  Masters /owners/ agents : port and HAZMAT notifications
  Local authorities (LCA) : VTS, MRCC, Port authorities, Coast guards, Pollution survey centres for incidents or accidents
  AIS : on board AIS and shore based networks
  Data requesters
  Member States Authorities
  SSN needs a network and applications (national and central)

## Slide 4
European Index Server
MS A
MS B
Information relating to vessels and incidents is collected at a MS level. Then submitted to EIS (computer located at the Data Centre in Luxemburg) which indexes it, so that it can be further used by other MSs.

## Slide 5
Member States shall receive notifications that shall forward to the EIS
Port notifications
Hazmat notifications
Ship (MRS&AIS) notifications
Alert notifications
Security notifications
All notifications have a common
part (IMO, MMSI, Call Sign and
Name) plus additional information
as required by the Directives.
Waste notifications
Article 4 of Directive 2002/59
Article 13 of Directive 2002/59
Article 9 of Directive 2002/59
Article 16 of Directive 2002/59
Article 4 of Regulation 725/2004

## Slide 6: Port notification (Annex I – Directive 2002/59)
Information to be notified in accordance with Article 4 .
General information:
(a) ship identification (name, call sign, IMO identification number or MMSI number),
(b) port of destination;
(c) estimated time of arrival at the port of destination or pilot station, as required by the competent authority, and estimated time of departure from that port;
(d) total number of persons on board.

## Slide 7: SafeSeaNet Interfaces
The XML Interface
    The primary interface between Member states and SSN
    Consists of a set of XML messages fulfilling the needs for both Data Provider and Data Requester
    Pure XML message exchange
    Automatic communication
The Web Interface
    Browser-based Interface between Data Requesters and the rest of the SSN network
    Entry point for Member States that have not developed an XML messaging mechanism
    Manual communication
Notes: RED BOLD TITLES link to the detailed lists of customers under the specific categories EUROPEAN INSTITUTIONS, NATIONAL INSTITUTIONS and MULTINATIONALS

## Slide 8: Data Exchange / Send Notifications
  Port
  Used to notify SafeSeaNet that a given vessel is bound for a particular port with an estimated time of arrival and with a number of persons aboard.
  Ship
  Used to notify SafeSeaNet about a ship’s voyage and cargo information. A ship notification is essentially based on MRS or AIS message.
  Hazmat
  Used to notify SafeSeaNet that a given vessel carries dangerous goods and that the sender owns some detailed information about these dangerous goods.
  Security / waste
  Used to notify SafeSeaNet that the sender holds some security / waste information about a given vessel.
  Alert
  Used to notify SafeSeaNet that the sender holds some information about specific incidents like SITREP, POLREP, Waste, lost/found containers. An alert can be linked or not to a particular vessel.
Notes: RED BOLD TITLES link to the detailed lists of customers under the specific categories EUROPEAN INSTITUTIONS, NATIONAL INSTITUTIONS and MULTINATIONALS

## Slide 9
Data exchange / Send Notifications
Data
Provider
SafeSeaNet
Core
System
Send
Notifications
Notes: RED BOLD TITLES link to the detailed lists of customers under the specific categories EUROPEAN INSTITUTIONS, NATIONAL INSTITUTIONS and MULTINATIONALS

## Slide 10
Data exchange / information Requests
  Port
  Is used to get detailed information about a given port notification. As SafeSeaNet holds the complete information of a port notification, there’s no need to ask more information to the Member State (data provider) having originally sent the port notification. Therefore, SafeSeaNet will also act as data provider for the port notification information request.
  Hazmat
  Ship
  Alert
  Security / waste
  Upon receiving such request, SafeSeaNet will ask the actual data provider to send him the detailed information. SafeSeaNet will then send it back to the data requester.
Notes: RED BOLD TITLES link to the detailed lists of customers under the specific categories EUROPEAN INSTITUTIONS, NATIONAL INSTITUTIONS and MULTINATIONALS

## Slide 11
Data exchange / Information Requests
SafeSeaNet
System
Data
Provider
Data
Requester
        MS2SSN_Req
        SSN2MS_Req
        SSN2MS_Res
        MS2SSN_Res
Notes: RED BOLD TITLES link to the detailed lists of customers under the specific categories EUROPEAN INSTITUTIONS, NATIONAL INSTITUTIONS and MULTINATIONALS

## Slide 12
13/02/2008 10:00
Lisbon
Port of Departure
European SafeSeaNet System
European Commission (DIGIT)
Hazmat Request
16/02/2008 11:00
Hamburg
Next Port of Call
SafeSeaNet Browser
Web User Interface
Vessel Identification
IMO : …………….
MMSI : …………….
Select the type of message
Port Reporting
Ship Reporting
Hazmat Reporting
Alert reporting
Incident
Submit
14/02/2008 23:00
MRCC Jobourg
Incident Reported
1234567
237124000


## Slide 13: XML messages structure and content
Root Element
Header Element
Body Element
Gives the name of the XML message
e.g. MS2SSN_Port_Not,
SSN2MS_Hazmat_Req etc.
Contains the “non-business” information e.g.
The sender of the message,
The time the message was sent,
Correlation IDs to relate messages,
The result of the processing of a request/notification message.
Contains the “business” information
In notification messages – the notification data
In request messages – the search criteria
In response messages – the search criteria of the
request and the notification
details
Notes: RED BOLD TITLES link to the detailed lists of customers under the specific categories EUROPEAN INSTITUTIONS, NATIONAL INSTITUTIONS and MULTINATIONALS

## Slide 14: XML message validation
The XML Schema definition
specifies how to formally describe the elements of the SSN XML messages
  The XML message is well formed (compliant with the XML syntax rules)
  The elements of the XML message are valid (based on the specifications)
Enforcement of business rules
Business rules : applied in the XML schema
some examples of business rules:
  At least one of IMO number, MMSI number must exist in the search criteria element
  The location code specified in the NextPortOfCall attribute must be a valid one
  The vessel specified in a notification message must not be banned
  When an XML message is not compliant with a business rule, a corresponding exception is
  arisen and a relevant message is sent back to the user
Notes: RED BOLD TITLES link to the detailed lists of customers under the specific categories EUROPEAN INSTITUTIONS, NATIONAL INSTITUTIONS and MULTINATIONALS

## Slide 15: Message processing
When the SafeSeaNet receives
  a MS2SSN_<SSN_Tx_Type>_Not, or
  a MS2SSN_<SSN_Tx_Type>_Req, or
  a MS2SSN_<SSN_Tx_Type>_Res
The following actions are applied:
Validation of the XML message
Binding of the XML message to the relevant business object
Checking of the user’s access rights
Creation of a log entry
Notes: RED BOLD TITLES link to the detailed lists of customers under the specific categories EUROPEAN INSTITUTIONS, NATIONAL INSTITUTIONS and MULTINATIONALS

## Slide 16: Processing of Notification messages
In case the XML message is a MS2SSN_<SSN_Tx_Type>_Not message
The following specific actions are applied:
Storing of the notification in the database
Checking of the vessel’s information, specified in the notification and if is needed update vessel’s information in the database, or create a new vessel in the database
Creation and sending of an SSN_Receipt message to the DataProvider
Notes: RED BOLD TITLES link to the detailed lists of customers under the specific categories EUROPEAN INSTITUTIONS, NATIONAL INSTITUTIONS and MULTINATIONALS

## Slide 17: Send Notifications Process
XML Messages
    MS2SSN_<SSN_Tx_Type>_Not
    XML notification message sent from Data Provider to SafeSeaNet.
    SSN_Receipt
    XML message sent from SafeSeaNet to Data Provider as positive or
    negative acknowledgement of the XML notification message
The Status code and Status message attributes of the SSN_Receipt are used to give the result of the processing of a SafeSeaNet xml message
Synchronous exchange of XML Messages
The XML messages sent over the same HTTP(S) connection
Status Code | Description
OK | The notification has been successfully proceeded
Invalid format | The xml message is not valid
Access Denied | The user is not allowed to send the corresponding message or does not exist
Server Error | The corresponding message has not been successfully proceeded due to a server problem
Notes: RED BOLD TITLES link to the detailed lists of customers under the specific categories EUROPEAN INSTITUTIONS, NATIONAL INSTITUTIONS and MULTINATIONALS

## Slide 18
Messages flow
Data
Provider
SafeSeaNet
System
DB
Process
MS2SSN_<SSN_Tx_Type>_Not
SSN_Receipt
If Notification is valid
<SSN_Tx_Type> can either be:
Port (Port notification)
Hazmat (Hazmat notification)
Ship (Ship notification)
Alert (Alert notification)
Security/waste (Security/ waste notification)
Check SSN_Receipt
(ACK or NACK)
Notes: RED BOLD TITLES link to the detailed lists of customers under the specific categories EUROPEAN INSTITUTIONS, NATIONAL INSTITUTIONS and MULTINATIONALS

## Slide 19: Processing of Request messages
In case the XML message is an MS2SSN_<SSN_Tx_Type>_Req message
The following specific actions are applied:
Storing of the Header of the request in the database plus an uuid
Universal Unique Identifier (uuid) generated by the central SafeSeaNet system for identifying a transaction initiated by an incoming MS2SSN_<SSN_Tx_Type>_Req XML message
Searching of the corresponding notification to this request in the SSN database
Depending on the notification’s data the SSN system
  Opens a new http(s) connection and sends an SSN2MS_<SSN_Tx_Type>_Res to the DataRequester (SSN act as DataProvider)
  Note: This action is always followed in case of MS2SSN_Port_Req
  Or
  Opens a new http(s) connection and send an SSN2MS_<SSN_Tx_Type>_Req to the DataProvider that owns the notification details
  Note: In the header of this message the SSNRefId attribute is added for reference reasons. The value of the SSNRefId is the previous uuid
If a notification is not found then a new http(s) connection is opened and an SSN2MS_<SSN_Tx_Type>_Res is sent to the DataRequester with StatusCode=“NotFound”
Notes: RED BOLD TITLES link to the detailed lists of customers under the specific categories EUROPEAN INSTITUTIONS, NATIONAL INSTITUTIONS and MULTINATIONALS

## Slide 20: MS2SSN_Port_Not.xml message
http://www.emsa.europa.eu/Docs/ssn/ssn-xmlmessagingrefguide-01_64.pdf

## Slide 21: Processing of Response messages
In case the XML message is an MS2SSN_<SSN_Tx_Type>_Res message
The following specific actions are applied:
Storing of the Header of the response in the database
Based on the SSNRefId in the header of the response message, SSN finds out the initial request (MSRefId) and the URL address of the DataRequester
Opens a new http(s) connection and sends an SSN2MS_<SSN_Tx_Type>_Res to the DataRequester containing the requested notifications details
Notes: RED BOLD TITLES link to the detailed lists of customers under the specific categories EUROPEAN INSTITUTIONS, NATIONAL INSTITUTIONS and MULTINATIONALS

## Slide 22: Architecture Overview
Notes: RED BOLD TITLES link to the detailed lists of customers under the specific categories EUROPEAN INSTITUTIONS, NATIONAL INSTITUTIONS and MULTINATIONALS