## Slide 1
<number>
SSN extension
to the IEC 61162 protocol
Oslo 1 March 2010
Notes: <number>

## Slide 2: Introduction
STIRES an enhancement to SafeSeaNet system
STIRES will interface with several existing and planned systems
- such as the existing AIS systems of the MS and non MS
- regional AIS servers
- existing SSN core system
STIRES interfaces to three RS collect AIS data provided by the MS instead of interfacing directly each MS
A software application- National Proxy (NPR) developed to facilitate the connection RS /STIRES server
The NPRs installed at the RS (typically in a redundant configuration) and manages the secure connection
Goal : distribute to participating countries, the full real-time AIS information picture, enhanced with selected data stored in SSN

## Slide 3: Use of CB in STIRES
The standard IEC 61162 protocol used for the exchange of AIS data between RS and STIRES
All 3 RS comply to IEC 61162
IEC 61162 standard, was primarily designed for on-board AIS equipment
Serious drawbacks when used in complex environments like SSN
STIRES and NPR are both supporting the Comment Block (CB) extension
IEC 62320-1 standard defines the AIS Base Stations interface
CBs are already used in SSN to extend standard IEC 61162 AIS messages with complete timestamp information

## Slide 4: New SSN requirements
SSN is expected to become the main EU service for the collection and distribution of vessel related information
STIRES NPRs may become a convenient mean to distribute data collected from sources other than terrestrial AIS (like LRIT, VTS, satellite AIS, VMS, etc) to National and/or Regional Systems
Standard IEC protocol should be appropriately extended
Proper distribution policy may be applied when appropriate

## Slide 5: Data Distribution Plan
Third countries in the STIRES : RF already delivering AIS data to the RSs
STIRES should implement a DDP to reflect the agreements between non EU countries and MSs
EMSA needs to know the originator country for each AIS message the RS are delivering to STIRES
The same applies to RSs to distribute AIS data received from STIRES to each connected country according to the DDP (if decided so)
IEC 61162 protocol does not identify the originator or specify the recipients: an appropriate extension is for customizable access rights

## Slide 6: Distribution of LRIT data
SSN will integrate LRIT data provided by the EU LRIT D/C
STIRES capable to distribute LRIT data to the NPRs using pseudo-AIS messages (LRIT information encoded as AIS IEC 61162 sentences)
Two main issues:
- Current SSN implementation of AIS pseudo-messages 1, 2 and 3 featuring LRIT data, uses a reserved for future use value for the "Navigational Status" to allow applications at Regional and National level to distinguish LRIT from AIS data. The forthcoming revision in the "Navigational Status" field, all the 16 values are associated to a status (ambiguity?)
- Strict access rights apply to LRIT data (the protocol should be extended to identify the originator and the recipients for each message).

## Slide 7: Distribution of data from other sensors
SSN will integrate other data coming from different types of sensors ( VTSs, VMSs, Satellite AIS, SAR images)
Additional information may be distributed to users through the NPRs using pseudo-AIS messages (as LRIT data).
Two issues :
- How to extend the pseudo AIS message with the information on the type of sensor which generated the data is needed.
- Access rights may apply to this additional information. If those messages are delivered to RSs and MSs through the NPRs, how should be provided in order to allow local administration to apply the proper policies.

## Slide 8: Amendments to the exchange protocol
CBs defined in the IEC 62320-1 standard for AIS BS becomes an extension to the IEC 61162 protocol
CB is a list of parameter code preceding the related IEC 61162 sentence
IEC 62320-1 standard defines a dictionary of parameter codes:
  ‘c’: Time in seconds (time tag used to provide a complete timestamp with the AIS message)
  ‘d’: destination (Identification of intended listener device or process for the attached sentence)
  ‘s’: source. Identification of the talker device or process for the attached sentence.
  ‘i’: information. This is free form text using valid characters

## Slide 9: Amendments to the exchange protocol
Parameter ‘c’ is already used in SSN to extend the AIS messages with complete time information
Parameters ‘d’ and ‘s’ are intended to identify talker IDs of software processes and hardware devices
Parameter ‘i’ can be freely used to embed additional information to the message
Basic question
How to use the information parameters to extend the (pseudo) AIS message with the required information mentioned before?
Answer
The use parameter ‘i’

## Slide 10: How to use parameter ‘i’
Five tags defined to associate information on : the sensor type, originator, recipients, enrichment and port of destination related to the linked (pseudo) AIS message:
Tag <S> used to specify which kind of sensor/system provided the information (eg values A, L, R, S, V indicate AIS, LRIT, RADAR/VTS, S-AIS, VMS). Other values may be introduced in the future. May be omitted for true AIS messages to save bandwidth.
Tag <O> used to specify the originator(s) of the information which may be countries, LRIT users, ports, etc. Reduce the length of the identifiers using codes.
Tag <R> used to specify the recipient(s) of the information which may be countries, LRIT users, ports, etc.
Tag <E> used to specify the enrichment of the information. It should contain a string including the letters A,B,H,S depending on whether there are respectively Alert, Banned vessel, Hazmat or Single Hull Tanker notifications pending on the vessel.
Tag <P> is used to specify the Port of Call for the vessel. It should contain a string with the LOCODE of the port. This information can be locally used also to perform appropriate filtering when distributing data to countries or port authorities.

## Slide 11: Example
How to encapsulate the following information in a CB:
  Type of sensor = AIS
  Port of destination = Naples, Italy
  Originator = Italy
  Recipients = Italy, France, Spain
  Enrichment = Is Banned, Is Hazmat
The content of comment block parameter ‘i’ will be the following using MIDs to identify the countries:
<S>A<S/><P>ITNAP<P/><O>247<O/><R>247 226 224<R/><E>BH<E/>