## Slide 1
<number>
Development of AIS network data exchange in the North Atlantic Sea region
Oslo 2 March 2010
Lazaros Aichmalotidis
Unit C.2 – Vessel Traffic and reporting Services

## Slide 2: Why regional systems
<number>
a. Traffic management and real-time monitoring
• Early warning
• Target tracking
• Organize and coordinate SAR operations over greater areas
• Redundancy potential
b. Semi-automatic ship reporting
c. Risk assessment and planning for efficient vessel traffic
d. Accident and incident investigation
e. Benefits from combining data at central level
Notes: <number>
Regional AIS networks – What for?
  To explain the concept of the regional AIS servers (what for?) mention that they give flexibility to the states belonging to a specific region to develop their system according to the local needs
Regional AIS networks – Current State of play
  To present what is available today in the other regions (HELCOM, North Sea, Med Sea, North Atlantic – still under discussion)
Role of EMSA in the development of regional AIS networks
  Explain the role of EMSA in the development of regional systems (especially in the Med AIS)
Regional AIS networks – the collaboration agreement
  Taking the example of the Med AIS and explain which are the basic things to be agreed (on technical basis) (eg standards, update rate etc).
  Make a special reference to the agreement structure
Regional AIS networks – Technology considerations
  Why standardisation is needed? (Because minimum standards have to be followed by all if they want a link between regions)
Regional AIS networks integration at European level (STIRES )
  Present the EMSA plans for STIRES and integrated systems
Future prospects for STIRES – Integration of additional AIS servers
  in brief since the key issue for us and them is to develop a Black Sea AIS system but we should not exclude the possibility once agreement will be reached to integrate them at EU level)
Baltic Sea AIS regional server – The EMSA role
  What EMSA can offer to the Black Sea countries (management, coordination since we have the know how)
Baltic Sea AIS regional server – A potential road map
  What do they need to do? (create a working group leaded by EMSA with the objective to ….. (look at the terms of reference of the MED AIS))
Baltic Sea AIS regional server – Financing the project
  Financial support (is an issue that has to be further clarified)

## Slide 3
<number>
Safety
SAR
Security
Benefits (why regional networks)
Accident Investigation
Pollution prevention
Vessel Traffic Analysis
Traffic Efficency
Traffic monitoring
Pollution detection
Cooperation

## Slide 4: System overview
<number>
AIS regional server is intended to:
collecting AIS data in real time
distributing to all of the countries
storing AIS data at regional level
visualizing traffic image on adequate cartography
as in other regions
National Proxy takes care of:
management of physical connection,
exchange and down-sampling of messages sent from each AIS
National system to the regional server

## Slide 5: Architecture
<number>
Regional system - two separate software modules:
inside the National DMZ of each participant State (enables
AIS data exchange between each National system and the
Regional server)
on servers located in the Regional centre. Main services :
- collecting /distributing AIS data from/to the Proxy;
- storing AIS data in the Regional database;
- retrieving / analysing the stored AIS data and display in
predefined reports, layered over charts (GIS).
Internet used for connecting the RS with the National proxies

## Slide 6: Architecture
<number>

## Slide 7: Functional Characteristics of the National Proxy
<number>
National Proxy main function: Establish and manage the connection between the National system and the RS.
Main characteristics:
Proxy guarantees a secure connection to the Regional server
Data exchanged between the Proxy and the Regional server
encrypted through the use of SSL/TSL connections.
Format of AIS data: IEC 61162-1, IEC/PAS 61162-100 and
IEC/PAS 61162-101 standards.

## Slide 8: Functional Characteristics of the National Proxy
<number>
The Proxy filters AIS data coming from the AIS
National server
ITU messages includes the messages carrying
static, dynamic and voyage AIS data (i.e. ITU
messages 1, 2, 3, 4, 5). Messages 9, 18, 19, 24A
and 24B (SAR and class B AIS) (f)
Time window 360 seconds by default (possible to
change this value).
Minimum requirements for Internet connection
bandwidth for all regional AIS data :200kbits/s

## Slide 9: Functional Characteristics of the National Proxy
<number>
Proxy performs a down-sampling of the National AIS data
before sending data to Regional server.
For each AIS target (identified by MMSI) a single set of data
should be forwarded to the Regional server
T1
Message
MMSI1
Message
MMSI1
Message
MMSI1
Message
MMSI1
T2
T3
T4
T5
Message
MMSI1

## Slide 10: Hardware and basic software requirements
<number>
Minimum H/W and S/W requirements of the National proxy:
Processor: 2.66 GHz Dual core Intel Xeon 5150;
RAM memory: 4 GB DIMM PC2-5300;
Multimedia driver: slim line CD-RW/DVD ROM 24x;
Storage: 80 GB;
Network card: Gigabit network adapter;
Video Card;
Monitor, keyboard and mouse, USB ports;
Operating system: MS Windows XP.

## Slide 11: Regional server Functional Characteristics
<number>
Collection of data from the National Proxies;
- filtering of data to remove duplicates caused by repetitions of the same AIS track
Distribution of data towards the National Proxies;
- set different down-sampling rate for outgoing data (filtering criteria configurable)
Storage of data in the Regional database (two separate database)
- the first stores raw data, used to display the AIS picture or to perform the
playbacks (6 months).
- the second database for generation of statistical reports (5 years)
Displaying and statistical processing through the Web portal
- authorized users display Regional AIS data using Internet
- connection secured through one way SSL (https).
- display of AIS picture, playback of old AIS data, generation of statistical reports etc

## Slide 12: Regional server Functional Characteristics
<number>

## Slide 13
<number>
Time schedule

## Slide 14
<number>
Connections to Member States AIS networks
MS1 AIS
MS2 AIS
MS3 AIS
Baltic Region
North Sea
Region
Mediterranean
Region
North Atlantic
Region
EU AIS
National Level
Regional
Level
EU Level
MS4 AIS
MS5 AIS
. . . . .
S-AIS
Notes: <number>
Here we can see an example of the system concept linking the national systems in regional networks such as in the examples of the Baltic and North Sea.
Data is collected at national data distribution centres (servers), usually all of the data at or near the full rate.
Only a sample of the AIS messages are forwarded to the regional data at a sampled rate and only part of the message (depending upon MS requirements and including at a minimum, the position coordinates, identity and time stamp). The sampling rate in the Baltic is for example, once every 6 minutes.
Poor data is filtered out, duplicates are also removed.
In formation is relayed in ‘Real time’
“Real time” exchange should be understood in the context of data delivered end-to-end, non-stop, one vessel report after another. The data originated by the on board AIS, is picked up by the MS shore based AIS network and is relayed to the regional or EU network, at a sampled rate, without any delay. This does not mean that all messages received by the national centre are relayed to the regional or EU server.

## Slide 15
<number>
Integration in SafeSeaNet (2010)
MS1 AIS
Region
Baltic
Region
North Sea
Region
Mediterranean
Region
North Atlantic
EU AIS
MS2 AIS
MS3 AIS
MSx AIS
SSN EIS
NCA1
NCA2
National Level
EU Level
Regional
Level
NCA2
MS4 AIS
MS5 AIS
. . . . .
Composite
traffic image
LRIT
Other
sensors
LRIT
Data Centre
Satellite
Imagery
Notes: <number>
Taking this up one further level, the STIRES concept foresees the development of an EU level.
The information that would be relayed to and stored at the EU server should be reduced to the necessary minimum (ship name, IMO number, position and time stamp). Considering that the information in the EU server is based on the existing short range traffic monitoring infrastructures of the Member States (AIS), the term SRIT (Short Range Identification and Tracking) is the proposed acronym.
The AIS data formats at regional and EU level should follow the existing IEC formats (IEC 61993-2 and 61162-1 sentences) and there would be no need to convert them into another format for exchange purposes within STIRES module.

## Slide 16
<number>
<number>
ALERT
HAZMAT
INSPECTION
PORT
LRIT
Back

## Slide 17
HELCOM
AIS server
North Sea
AIS server
Mediterranean
AIS server
STIRES server
Black Sea
Server
Northern N.Atlantic server
Groenland
Feroe. Island
Canada